Land Rover Defender - Checklist

| Area | Check | Result |
| --- | --- | --- |
| Ownership | Number of previous owners |  |
|  | Previous uses |  |
|  | Why being sold (enquire if owned for less than a year) |  |
|  | Review V5 ‘log book’ – makes sure tallies with the owner |  |
|  | Check previous details with ‘AA Data Check’ or ‘HPI’ (check not an insurance write-off) |  |
|  | Review previous MOTs – check to make sure if was serviced regularly |  |
|  | Review ‘Service Book’ – should be stamped (if reasonable new) |  |
| Initial Checkout - if significant failure, leave car | Exterior - Look at panels and sill area beneath doors – a few dents inevitable, lots of dents equals rough use |  |
|  | Interior - Carpets clean or scuffed, seats, headlining, dashboard |  |
|  | Bonnet - Open - Filthy, wires hanging loose? - Low coolant, hydraulic levels pitch black oil on dipstick |  |
| Chassis | Dents and gouges – caused by contact with rocks. Lots of dents point to a hard life |  |
|  | Check for levels of rust, check if filler has been used anywhere |  |
|  | Check if repair sections or plates have been welded in |  |
|  | Front crossmember – dents or rust |  |
|  | Back crossmember – dents or rust |  |
|  | Bulkhead – check for rust. Check inside the cab and from beneath and above the engine bay |  |
| Bodywork | Slight bodywork corrosion expected |  |
|  | Doors – inspect hinges, inside and out |  |
|  | Rear door – check hinges, rear window wash wipers and heating elements. |  |
| Suspension | Test drive- general sloppiness? |  |
|  | Does the land rover sag anywhere? Not a big issue – springs and dampers easy to replace |  |
| Steering | Poor steering noticed while driving |  |
|  | Chrome-plated front swivels – surface pitting needs to be replaced |  |
|  | Power steering – check for leaks before and after test drive |  |
| Transmission | Some free-play expected. Bad needs to be reviewed. Noticed on start off and changing gear. Simulate traffic. |  |
|  | Test for smooth changes in all gears – check doesn’t jump out of gear when accelerating. |  |
|  | Repeat with low ratios – high-low may be stiff. |  |
|  | Check hand brake on a slope |  |
|  | Check beneath vehicle for oil leaks from axle differentials and main and transfer gear boxes. |  |
| Engine | Check for serious oil leaks, particularly from seals |  |
|  | Check for smoke from exhaust on start-up – should be white or blue and should disappear quickly |  |
|  | Check if engine driven hard (full revs for each gear change, driving flat out on open road) – valve or piston wear (blue exhaust smoke and/or serious oil leaks), turbocharger wear, intercooler problems, cracked blocks and heads. |  |
|  | Timing Belt Changes – find out when last changed (300 Tdis have required modification – has this been done). |  |
| Interior | Have a general look at condition and beneath seat covers |  |
|  | Check for leaks or condensation problems. |  |
| Smoke Signals | If more than a modest mini puff of black smoke on start-up – injectors are worn – easy and cheap to repair |  |
|  | White smoke – excess fuel, problems with distributor pump |  |
|  | Blue smoke on start-up or overrun – wear in the valve guides and seals |  |
|  | Blue smoke persists – wear in the bores, piston and piston rings developed serious wear or broken |  |
|  | Most serious problem may be cylinder wear – to check, remove engine breather cap while engine is running, and slowly increase the revs. If the bores, pistons and rings are worn beyond normal tolerances they will allow the crankcase to pressurize, blowing oil mist or smoke out of the cap. Major strip down required. |  |